## Slide 1: Internet of Things with the atmega328p, A motion detector
Brandon Wade
wadeb1@unlv.nevada.edu
UNLV College of Engineering
CPE 301 – Final Project

## Slide 2: Aim and Accomplishments
The aim of this project was to create an internet of things (IoT) devices that would read (MPU6050) sensor data and broadcast this data (vis ESP8266) to a cloud service (ThingSpeak)
This task was accomplished and accelerometer values were successfully read from the MPU6050 sensor and displayed to the cloud.
Using this raw data, one can detect any kind of motion. For example, setting up this device to the front door of your house could show you a log of if and how often your door is opened, therefore having application in home security.

## Slide 3: Schematics
http://imgur.com/zrvD4rW

## Slide 4: Design Stages - Components
Hardware | Software
ATMega328P | Atmel Studio 6.0
MPU6050 Sensor | Putty
ESP8266 | ESPlorer
SparkFun USB to Serial Breakout – FT232RL | ThingSpeak
BreadBoard | 

## Slide 5: Design Stages - Interfaces
ATMega328P to MPU6050 – I2C
  0x3B – X acceleration
  0x3D – Y acceleration
  0x3F – Z acceleration
ATMega328P to ESP8266 – USART
  8-bit data
  BAUD = 115200 (required for AT)
  TX used only
ESP8266 to WiFi
  AT firmware used

## Slide 6: Design Stages – Cloud Service
ThinkSpeak cloud service was used
  3 fields for x, y, and z acceleration values were updated synchronously.
  Updated every 20 seconds
  Data represented graphically

## Slide 7: Code Development - Initialization
USART initialized to send 8 bit data with a BAUD of 115200
I2C initialized with no prescaler
ESP8266 programmed to automatically connect to desired WiFi network (mobile hotspot in my case)
MPU6050 initializes, waking up sensor, setting frequency, enables FIFO, etc
MPU6050 initially reads and averages data for calibraiton

## Slide 8: Code Development – Data Collection
ATMega328P reads MPU6050 registers periodically for accelerometer values.
Values are averaged (three samples on each read cycle) and compared to calibrated value
Data is then converted from floats to printable types
  Floats were not printing correctly and therefore values were converted into int components and then printed

## Slide 9: Code Development - Visualization
AT commands used to write data to ThingSpeak
  Start TCP Connection: AT+CIPSTART=4,\"TCP\",\"184.106.153.149\",80\r\n
  Channel initialization: AT+CIPSEND=4,75\r\n
  Send data via channel:
  GET /update?key=7PA0P9DMZOLYS1JR&field1=%i.%i%i&field2=%i.%i%i&field3=%i.%i%i
  Close channel: AT+CIPCLOSE\r\n
ThingSpeak then receives data and graphs it versus time
  http://imgur.com/Avt1Kj8

## Slide 10: Demo
https://www.youtube.com/watch?v=RngmWc71sFk

## Slide 11: References
http://rancidbacon.com/files/kiwicon8/ESP8266_WiFi_Module_Quick_Start_Guide_v_1.0.4.pdf
https://mcuoneclipse.com/2014/12/14/tutorial-iot-datalogger-with-esp8266-wifi-module-and-frdm-kl25z/
https://www.cdiweb.com/datasheets/invensense/MPU-6050_DataSheet_V3%204.pdf
http://www.atmel.com/images/atmel-8271-8-bit-avr-microcontroller-atmega48a-48pa-88a-88pa-168a-168pa-328-328p_datasheet_complete.pdf
MPU6050_helper codes

## Slide 12: Questions?